## Slide 1: Chapter 5
Optical Fibers

## Slide 2
Core n1
Clade n2
θ
θ
θ
θ
θ
θ
Optical Fiber Structure
1 – Core with refractive index n1
2 – Clade with refractive index n2
n1(core) > n2(clade)
r

## Slide 3
1 - Core
2 - Cladding
3 - Buffer
4 - Jacket
Optical Fiber Structure

## Slide 4: Advantages of Optical Fiber
1- light travels much faster than an electrical system (as with a metal wire system), thereby allowing faster reception and delivery of information.
2- Fiber optic schemes have a much higher capacity for bandwidth than those that are more traditional.
3- Fiber optics, on the other hand, is not affected by external electrical signals, since data is transmitted with light. Its immunity to electromagnetic interference is another huge advantage over metal wire and coaxial channels.

## Slide 5: Advantages of Optical Fiber
4-Optical systems also offer more security than traditional mediums.
5-Fiber optic systems are one of the safest forms of data transmission in terms of fire prevention
6-Fiber optic systems are much more efficient than coaxial and copper mediums because there is far less loss of data
7-The cladding used in this science of light transmission also greatly increases the effectiveness of data transmission. Because of this innovation, coupled with the total internal reflection, there is no crosstalk between cables.

## Slide 6: Modes
The light traveling down the fiber is a group of electromagnetic waves occupying a small band of frequencies within the electromagnetic spectrum.
The two components, the electric field and the magnetic field, form patterns across the fiber. These patterns are called modes of transmission.

## Slide 7
Types of Optical Fibers
r
n
ncore
nclade
1- Single mode fiber
Notes: <number>

## Slide 8
Types of Optical Fibers
r
n
ncore
nclade
2- Multimode Step Index
Notes: <number>

## Slide 9
Types of Optical Fibers
r
n
nclade
2- Multimode Graded Index
Notes: <number>

## Slide 10: Numerical Aperture NA
θ
θ
θ
θ
θ
θ
Core
Clade
θmax
θmax
θmax: Acceptance Angle

## Slide 11: Numerical Aperture NA
Core n1
Clade n2
θmax
θmax
Light Acceptance
Cone
Outside medium n

## Slide 12: Attenuation
1-By Scattering

## Slide 13: Attenuation
2-By absorption
Any impurities that remain in the fiber after manufacture will block some of the light energy. The worst culprits are hydroxyl ions and traces of metals.
The hydroxyl ions are actually the form of water which caused the large losses at 1380 nm
metallic traces can cause absorption of energy at their own particular wavelengths. These small absorption peaks are also visible.
In both cases, the answer is to ensure that the glass is not contaminated at the time of manufacture and the impurities are reduced as far as possible.

## Slide 14: Transmission Windows
Medium distance
data
Long distance
telecoms
Loss due to water
absorption at λ=1380nm

## Slide 15: Transmission Windows
Medium distance
data
Long distance
telecoms
850 nm
window
1300 nm
window
1550 nm
window

## Slide 16: Fiber performance
z=0
z=L
Dispersion
z=0
z=L
Attenuation

## Slide 17: 1- Chromatic dispersion
We know that light of different wavelengths is refracted by differing amounts. The refractive index, and hence the speed of the light, is determined to some extent by its wavelength.
Each component wavelength travels at a slightly different speed in the fiber.

## Slide 18: 1- Chromatic dispersion
θ1
Core
Clade
θ2
Each component wavelength travels at a slightly different speed in the fiber.

## Slide 19: 1- Chromatic dispersion
This causes the light pulse to spread out as it travels along the fiber and hence causes dispersion.

## Slide 20: 2- Modal dispersion
Modal dispersion is the result of different modes (rays) traveling at different paths.
Imagine we launch two different rays of light into a fiber. Now, since both rays are traveling in material of the same refractive index they must be moving at the same speed.
Ray A, will travel a longer distance than the other, Ray B

## Slide 21: 2- Modal dispersion
Dispersion causes the pulses to spread out and eventually they will blend together and the information will be lost

## Slide 22: 2- Modal dispersion
Dispersion causes the pulses to spread out and eventually they will blend together and the information will be lost

## Slide 23: How to overcome Modal dispersion?
1-We could make this degree of dispersion acceptable by simply decreasing the transmission frequency and thus allowing larger gaps between the pulses.

## Slide 24: How to overcome Modal dispersion?
2- Modal dispersion is the result of different modes (rays) traveling at different paths. The easy way to avoid this is to have only one mode in a single mode fiber.
3- We could redesign the fiber to eliminate the modal dispersion. This strategy is called graded index optic fiber.

## Slide 25: Graded Index Fiber
r
n
nclade

## Slide 26: Graded Index Fiber
Total internal reflection
occurs here
r
n

## Slide 27: Bandwidth-Distance Product
1-Because the effect of dispersion increases with the length of the fiber, a fiber transmission system is often characterized by its bandwidth-distance product, often expressed in units of MHz×km or gigahertz×kilometer (GHz×km).
2-This value is a product of bandwidth and distance because there is a tradeoff between the bandwidth of the signal and the distance it can be carried.
3-For example, a common multimode fiber with bandwidth-distance product of 500 MHz×km could carry a 500 MHz signal for 1 km or a 1000 MHz signal for 0.5 km.